## Slide 1: KINEMATIC PAIRS and LINKAGES
Kinematic Pairs
Kinematic pairs are of different type e.g. turning pair, sliding pair, screw pair etc. However, depending on contact between the elements of a pair it is classified as either a higher pair or a lower pair based on whether the elements of the pair have a point/line contact or a surface contact.
Important: Go through books to understand the operations of different kinematic pairs.
Linkages
A mechanism which has only lower pairs is called a linkage.
Thus a ‘simple engine mechanism’ is a ‘four-bar single-slider chain’.

## Slide 2: Inversion of Mechanisms
Inversion
Every mechanism has a fixed link called the frame. It is possible to obtain from one kinematic chain a number of different mechanisms; if one mechanism is converted into another by fixing an alternative link, the process is described as inversion. When different links are chosen as the frame for a given kinematic chain, the relative motions between the various links are not altered, but their absolute motions (with respect to frame) may be changed drastically.
Important: Go through books to study how different inversions are obtained from some known mechanism (like slider-crank mechanism).

## Slide 3: Mobility (DoF of Mechanisms)
Mobility
In the design or analysis of a mechanism one of the first concerns is the number of degrees of freedom, also called the mobility of the device (the difference of mobility and movability may be noted). The mobility of a mechanism is the number of input parameters (usually pair variables) that must be controlled independently in order to bring the device into a particular position.
Kutzbach criterion for the mobility of a planar mechanism is given by m = 3(n-1) – 2j1 – j2, where m is mobility, n is number of links, j1 and j2 are the number of pairs with single and double degrees of freedom respectively.
However, for planar mechanisms with only single-degree-of-freedom joints where the overall mobility of the mechanism is unity, the mobility criterion is named after Grubler. Putting j2 = 0 and m = 1 into Kutzbach criterion, Grubler’s criterion for planar mechanisms with constrained motion becomes, 3n – 2j1 – 4 = 0.
Important: Verify Grubler’s criterion for a slider-crank mechanism.

## Slide 4: Grashof’s law
When designing a mechanism to be driven by a motor, one has to ensure that the input crank can make a complete revolution. Grashof’s law states that for a planar four bar linkage, the sum of the shortest and longest link lengths cannot be greater than the sum of the remaining two link lengths if there is to be continuous relative motion between two members.
Verify the law yourself for a four-bar linkage.

## Slide 5: Different Mechanism
Though kinematic analysis of different mechanisms would be considered in our study, attention will be given to the four-bar linkage especially crank-and-rocker mechanism and reciprocating mechanisms like slider-crank mechanism and quick-return mechanism (e.g. Whitworth quick-return mechanism, also called the crank-shaper mechanism).
A measure of the suitability of the mechanism from this viewpoint, called advance-to-return-time ratio, is defined by the formula Q = (time of advance stroke)/(time of return stroke) and mechanisms with Q greater than unity are called quick-return mechanisms. A mechanism for which the value of Q is high is more desirable for such repetitive operations than one in which Q is lower.
Special Mechanisms: Indicator Diagram Mechanisms, Steering Mechanisms, Hooke Joint.
Some other important mechanisms are Geneva mechanism, toggle mechanism, oscillating mechanism, wrapping machine mechanism – refer to book.