## Slide 1
Lecture -31-34
Kinetics of particle
Energy, momentum, impulse

## Slide 2
Energy and Momentum method
The pogo stick allows the boy to change between kinetic energy, potential energy from gravity, and potential energy in the spring.
Accidents are often analyzed by using momentum methods.

## Slide 3
Introduction
Previously, problems dealing with the motion of particles were solved through the fundamental equation of motion,
The current chapter introduces two additional methods of analysis.
Method of work and energy: directly relates force, mass, velocity and displacement.
Method of impulse and momentum: directly relates force, mass, velocity, and time.

## Slide 4
Introduction
Forces and Accelerations
Velocities and Displacements
Velocities and Time
Newton’s Second Law (last chapter)
Work-Energy
Impulse-Momentum

## Slide 5
Work of a force
Differential vector is the particle displacement.
Work of the force is
Work is a scalar quantity, i.e., it has magnitude and sign but not direction.
Dimensions of work are
Units are

## Slide 6
Work of a force
Work of a force during a finite displacement,
Work is represented by the area under the curve of Ft plotted against s.
Ft is the force in the direction of the displacement ds

## Slide 7
Work of a force
Work of the force of gravity,
Work of the weight is equal to product of weight W and vertical displacement Dy.

## Slide 8
Work of a spring force
Magnitude of the force exerted by a spring is proportional to deflection,
Work of the force exerted by spring,
Work of the force exerted by spring is positive when x2 < x1, i.e., when the spring is returning to its un-deformed position.
Work of the force exerted by the spring is equal to negative of area under curve of F plotted against x,

## Slide 9
Work of a spring force
As the block moves from A0 to A1, is the work positive or negative? -ve
As the block moves from A2 to Ao, is the work positive or negative? +ve
Displacement is in the opposite direction of the force.

## Slide 10
Work of a gravitational force
Work of a gravitational force (assume particle M occupies fixed position O while particle m follows path shown),

## Slide 11
Principle of work and energy
Consider a particle of mass m acted upon by force
Integrating from A1 to A2 ,
The work of the force is equal to the change in kinetic energy of the particle.
Units of work and kinetic energy are the same:

## Slide 12
Principle of work and energy (application)
The bob is released from rest at position A1. Determine the velocity of the pendulum bob at A2 using work & kinetic energy.
Force acts normal to path and does no work.
Velocity is found without determining expression for acceleration and integrating.
All quantities are scalars and can be added directly.
Forces which do no work are eliminated from the problem.

## Slide 13
Principle of work and energy (application)
Principle of work and energy cannot be applied to directly determine the acceleration of the pendulum bob.
Calculating the tension in the cord requires supplementing the method of work and energy with an application of Newton’s second law.
As the bob passes through A2 ,

## Slide 14
Power and energy
Dimensions of power are work/time or force*velocity. Units for power are

## Slide 15
Problem-1
An automobile weighing 4000 lb is driven down a 5o incline at a speed of 60 mi/h when the brakes are applied causing a constant total breaking force of 1500 lb.
Determine the distance traveled by the automobile as it comes to a stop.
SOLUTION:
Evaluate the change in kinetic energy.
Determine the distance required for the work to equal the kinetic energy change.

## Slide 16
Problem-1
SOLUTION:
Evaluate the change in kinetic energy.
Determine the distance required for the work to equal the kinetic energy change.

## Slide 17
Two blocks are joined by an inextensible cable as shown. If the system is released from rest, determine the velocity of block A after it has moved 2 m. Assume that the coefficient of friction between block A and the plane is mk = 0.25 and that the pulley is weightless and frictionless.
SOLUTION:
Apply the principle of work and energy separately to blocks A and B.
When the two relations are combined, the work of the cable forces cancel. Solve for the velocity.
Sample Problem 2

## Slide 18
SOLUTION:
Apply the principle of work and energy separately to blocks A and B.
Sample Problem 2

## Slide 19
When the two relations are combined, the work of the cable forces cancel. Solve for the velocity.
Sample Problem 2

## Slide 20
Could you apply work-energy to the combined system of blocks?
Given: v1= 0, distance = 2 m, mk = 0.25
Note that vA = vB
What is T1 of the system?
What is the total work done between points 1 and 2?
What is T2 of the system?
Solve for v
Alternate Solution, Group Problem Solving

## Slide 21
A spring is used to stop a 60 kg package which is sliding on a horizontal surface. The spring has a constant k = 20 kN/m and is held by cables so that it is initially compressed 120 mm. The package has a velocity of 2.5 m/s in the position shown and the maximum deflection of the spring is 40 mm.
Determine (a) the coefficient of kinetic friction between the package and surface and (b) the velocity of the package as it passes again through the position shown.
SOLUTION:
Apply the principle of work and energy between the initial position and the point at which the spring is fully compressed and the velocity is zero. The only unknown in the relation is the friction coefficient.
Apply the principle of work and energy for the rebound of the package. The only unknown in the relation is the velocity at the final position.
Sample Problem 3

## Slide 22
SOLUTION:
Apply principle of work and energy between initial position and the point at which spring is fully compressed.
Sample Problem 3

## Slide 23
Apply the principle of work and energy for the rebound of the package.
Sample Problem 3

## Slide 24
A 2000 lb car starts from rest at point 1 and moves without friction down the track shown.
Determine:
the force exerted by the track on the car at point 2, and
the minimum safe value of the radius of curvature at point 3.
SOLUTION:
Apply principle of work and energy to determine velocity at point 2.
Apply Newton’s second law to find normal force by the track at point 2.
Apply principle of work and energy to determine velocity at point 3.
Apply Newton’s second law to find minimum radius of curvature at point 3 such that a positive normal force is exerted by the track.
Sample Problem 4

## Slide 25
SOLUTION:
Apply principle of work and energy to determine velocity at point 2.
Apply Newton’s second law to find normal force by the track at point 2.
Sample Problem 4

## Slide 26
Apply principle of work and energy to determine velocity at point 3.
Apply Newton’s second law to find minimum radius of curvature at point 3 such that a positive normal force is exerted by the track.
Sample Problem 4

## Slide 27
The dumbwaiter D and its load have a combined weight of 600 lb, while the counterweight C weighs 800 lb. Determine the power delivered by the electric motor M when the dumbwaiter (a) is moving up at a constant speed of 8 ft/s and (b) has an instantaneous velocity of 8 ft/s and an acceleration of 2.5 ft/s2, both directed upwards.
SOLUTION:
In the first case, bodies are in uniform motion. Determine force exerted by motor cable from conditions for static equilibrium.
In the second case, both bodies are accelerating. Apply Newton’s second law to each body to determine the required motor cable force.
Sample Problem 5
Force exerted by the motor cable has same direction as the dumbwaiter velocity. Power delivered by motor is equal to FvD, vD = 8 ft/s.

## Slide 28
In the first case, bodies are in uniform motion. Determine force exerted by motor cable from conditions for static equilibrium.
Free-body C:
Free-body D:
Sample Problem 5

## Slide 29
In the second case, both bodies are accelerating. Apply Newton’s second law to each body to determine the required motor cable force.
Free-body C:
Free-body D:
Sample Problem 5

## Slide 30
Sample Problem 6

## Slide 31
Sample Problem 6

## Slide 32
Packages are thrown down an incline at A with a velocity of 1 m/s. The packages slide along the surface ABC to a conveyor belt which moves with a velocity of 2 m/s. Knowing that mk= 0.25 between the packages and the surface ABC, determine the distance d if the packages are to arrive at C with a velocity of 2 m/s.
SOLUTION: The problem deals with a change in position and different velocities, so use work-energy.
Find the kinetic energy at points A and C.
Determine the work done between points A and C as a function of d.
Use the work-energy relationship and solve for d.
Draw FBD of the box to help us determine the forces that do work.
Group Problem Solving

## Slide 33
SOLUTION: Given: vA= 1 m/s, vC= 2 m/s, mk= 0.25
Find: distance d
Will use:
Draw the FBD of the block at points A and C
Determine work done A → B
Determine work done B → C
Group Problem Solving

## Slide 34
Determine kinetic energy at A and at C
Substitute values into
Divide by m and solve for d
Group Problem Solving

## Slide 35
If you wanted to bring the package to a complete stop at the bottom of the ramp, would it work to place a spring as shown?
Would the package ever come to a stop?
No, because the potential energy of the spring would turn into kinetic energy and push the block back up the ramp
Yes, eventually enough energy would be dissipated through the friction between the package and ramp.
Concept Quiz

## Slide 36
Potential Energy
The potential energy stored at the top of the roller coaster is transferred to kinetic energy as the cars descend.
The elastic potential energy stored in the trampoline is transferred to kinetic energy and gravitational potential energy as the girl flies upwards.

## Slide 37
Work of the force of gravity W=mg,
Work is independent of path followed; depends only on the initial and final values of Wy.
potential energy of the body with respect to force of gravity.
Units of work and potential energy are the same:
Choice of datum from which the elevation y is measured is arbitrary.
Potential Energy

## Slide 38
Previous expression for potential energy of a body with respect to gravity is only valid when the weight of the body can be assumed constant.
For a space vehicle, the variation of the force of gravity with distance from the center of the earth should be considered.
Work of a gravitational force,
Potential energy Vg when the variation in the force of gravity can not be neglected,
Potential Energy

## Slide 39
Work of the force exerted by a spring depends only on the initial and final deflections of the spring,
The potential energy of the body with respect to the elastic force,
Note that the preceding expression for Ve is valid only if the deflection of the spring is measured from its undeformed position.
Potential Energy

## Slide 40
A 20 lb collar slides without friction along a vertical rod as shown. The spring attached to the collar has an undeflected length of 4 in. and a constant of 3 lb/in.
If the collar is released from rest at position 1, determine its velocity after it has moved 6 in. to position 2.
SOLUTION:
Apply the principle of conservation of energy between positions 1 and 2.
The elastic and gravitational potential energies at 1 and 2 are evaluated from the given information. The initial kinetic energy is zero.
Solve for the kinetic energy and velocity at 2.
Sample Problem 7

## Slide 41
SOLUTION:
Apply the principle of conservation of energy between positions 1 and 2.
Position 1:
Position 2:
Conservation of Energy:
Sample Problem 7

## Slide 42
The 0.5 lb pellet is pushed against the spring and released from rest at A. Neglecting friction, determine the smallest deflection of the spring for which the pellet will travel around the loop and remain in contact with the loop at all times.
SOLUTION:
Since the pellet must remain in contact with the loop, the force exerted on the pellet must be greater than or equal to zero. Setting the force exerted by the loop to zero, solve for the minimum velocity at D.
Apply the principle of conservation of energy between points A and D. Solve for the spring deflection required to produce the required velocity and kinetic energy at D.
Sample Problem 8

## Slide 43
SOLUTION:
Setting the force exerted by the loop to zero, solve for the minimum velocity at D.
Apply the principle of conservation of energy between points A and D.
Sample Problem 8

## Slide 44
The impulse applied to the railcar by the wall brings its momentum to zero. Crash tests are often performed to help improve safety in different vehicles.
The thrust of a rocket acts over a specific time period to give the rocket linear momentum.
Impulsive Motion

## Slide 45
From Newton’s second law,
linear momentum
The final momentum of the particle can be obtained by adding vectorially its initial momentum and the impulse of the force during the time interval.
Dimensions of the impulse of a force are force*time.
Units for the impulse of a force are
Principle of Impulse and Momentum

## Slide 46
Force acting on a particle during a very short time interval that is large enough to cause a significant change in momentum is called an impulsive force.
When impulsive forces act on a particle,
When a baseball is struck by a bat, contact occurs over a short time interval but force is large enough to change sense of ball motion.
Non impulsive forces are forces for which is small and therefore, may be neglected – an example of this is the weight of the baseball.
Impulsive Motion

## Slide 47
An automobile weighing 4000 lb is driven down a 5o incline at a speed of 60 mi/h when the brakes are applied, causing a constant total braking force of 1500 lb.
Determine the time required for the automobile to come to a stop.
SOLUTION:
Apply the principle of impulse and momentum. The impulse is equal to the product of the constant forces and the time interval.
Sample Problem 9

## Slide 48
SOLUTION:
Apply the principle of impulse and momentum.
Taking components parallel to the incline,
Sample Problem 9

## Slide 49
A 4 oz baseball is pitched with a velocity of 80 ft/s. After the ball is hit by the bat, it has a velocity of 120 ft/s in the direction shown. If the bat and ball are in contact for 0.015 s, determine the average impulsive force exerted on the ball during the impact.
SOLUTION:
Apply the principle of impulse and momentum in terms of horizontal and vertical component equations.
Sample Problem 10

## Slide 50
SOLUTION:
Apply the principle of impulse and momentum in terms of horizontal and vertical component equations.
x
y
x component equation:
y component equation:
Sample Problem 10

## Slide 51
A 10 kg package drops from a chute into a 24 kg cart with a velocity of 3 m/s. Knowing that the cart is initially at rest and can roll freely, determine (a) the final velocity of the cart, (b) the impulse exerted by the cart on the package, and (c) the fraction of the initial energy lost in the impact.
SOLUTION:
Apply the principle of impulse and momentum to the package-cart system to determine the final velocity.
Apply the same principle to the package alone to determine the impulse exerted on it from the change in its momentum.
Sample Problem 11

## Slide 52
SOLUTION:
Apply the principle of impulse and momentum to the package-cart system to determine the final velocity.
x
y
x components:
Sample Problem 11

## Slide 53
Apply the same principle to the package alone to determine the impulse exerted on it from the change in its momentum.
x
y
x components:
y components:
Sample Problem 11

## Slide 54
To determine the fraction of energy lost,
Sample Problem 11

## Slide 55
The jumper approaches the takeoff line from the left with a horizontal velocity of 10 m/s, remains in contact with the ground for 0.18 s, and takes off at a 50o angle with a velocity of 12 m/s. Determine the average impulsive force exerted by the ground on his foot. Give your answer in terms of the weight W of the athlete.
SOLUTION:
Draw impulse and momentum diagrams of the jumper.
Apply the principle of impulse and momentum to the jumper to determine the force exerted on the foot.
Sample Problem 12

## Slide 56
Draw impulse and momentum diagrams of the jumper
Use the impulse momentum equation in y to find Favg
Given: v1 = 10 m/s, v2= 12 m/s at 50º,
Δt= 0.18 s
Find: Favg in terms of W
Group Problem Solving

## Slide 57
Use the impulse momentum equation in x and y to find Favg
Favg-x is positive, which means we guessed correctly (acts to the left)
Group Problem Solving

## Slide 58
Car A and B crash into one another. Looking only at the impact, which of the following statements are true?
The total mechanical energy is the same before and after the impact
If car A weighs twice as much as car B, the force A exerts on car B is bigger than the force B exerts on car A.
The total linear momentum is the same immediately before and after the impact
True
False
True
False
True
False
Group Problem Solving

## Slide 59
The coefficient of restitution is used to characterize the “bounciness” of different sports equipment. The U.S. Golf Association limits the COR of golf balls at 0.83
Civil engineers use the coefficient of restitution to model rocks falling from hillsides
Concepts

## Slide 60
Impact: Collision between two bodies which occurs during a small time interval and during which the bodies exert large forces on each other.
Line of Impact: Common normal to the surfaces in contact during impact.
Central Impact: Impact for which the mass centers of the two bodies lie on the line of impact; otherwise, it is an eccentric impact..
Direct Central Impact
Direct Impact: Impact for which the velocities of the two bodies are directed along the line of impact.
Oblique Central Impact
Oblique Impact: Impact for which one or both of the bodies move along a line other than the line of impact.
Impact
Impact involves (a) material deformation and recovery (in case three is no recovery, the deformation is plastic) and (b) generation of heat and sound.
Magnitude of force generated and duration of impact depend on: (a) shape of the bodies, (b) their velocities and (c) their elastic properties.
Types of Impact

## Slide 61
Bodies moving in the same straight line, vA > vB .
Upon impact the bodies undergo a period of deformation, at the end of which, they are in contact and moving at a common velocity.
A period of restitution follows during which the bodies either regain their original shape or remain permanently deformed.
Wish to determine the final velocities of the two bodies. Because the contact forces are equal and opposite during impact, the total momentum of the two body system is preserved,
A second relation between the final velocities is required.
Direct Central Impact
Before impact
During impact
(maximum deformation happens)
After impact

## Slide 62
Direct Central Impact
Plastic Impact:
If the material is absolutely inelastic, like putty, they continue to move together with the same speed.
Owing to the absence of elastic forces there is no tendency for rebound.
Elastic Impact:
Hardened polished steel or glass ball approach this condition if the local deformation during impact is not excessive.
In addition to the momentum equation (Eq. 1), total kinetic energy before and after impact is conserved.
Semi-elastic Impact:
In practice, there must be some loss of energy of the system during impact and therefore we expect some deviation from perfect elasticity.

## Slide 63
When e=0, Eq. (4a) reduces to Eq. (2), already derived for the case of plastic impact.
When e=1, we obtain Eq. (3) for elastic impact where the total energy and total momentum conserved.
Direct Central Impact
Newton’s experimental law states that :
Coefficient of restitution
Energy loss during impact
Note:

## Slide 64
Initial and Final velocities are not parallel.
Final velocities are unknown in magnitude and direction. Four equations are required.
The momentum of each particle in tangential direction is conserved.
Total momentum of the two particles in normal direction is conserved.
Oblique Central Impact
Normal components of relative velocities before and after impact are related by the coefficient of restitution.
Experimental evidence shows that

## Slide 65
Three methods for the analysis of kinetics problems:
  Direct application of Newton’s second law
  Method of work and energy
  Method of impulse and momentum. Select the method best suited for the problem or part of a problem under consideration.
Problems Involving Energy and Momentum

## Slide 66
A ball is thrown against a frictionless, vertical wall. Immediately before the ball strikes the wall, its velocity has a magnitude v and forms angle of 30o with the horizontal. Knowing that e = 0.90, determine the magnitude and direction of the velocity of the ball as it rebounds from the wall.
SOLUTION:
Resolve ball velocity into components normal and tangential to wall.
Impulse exerted by the wall is normal to the wall. Component of ball momentum tangential to wall is conserved.
Assume that the wall has infinite mass so that wall velocity before and after impact is zero. Apply coefficient of restitution relation to find change in normal relative velocity between wall and ball, i.e., the normal ball velocity.
Sample Problem 14

## Slide 67
Component of ball momentum tangential to wall is conserved.
Apply coefficient of restitution relation with zero wall velocity.
SOLUTION:
Resolve ball velocity into components parallel and perpendicular to wall.
n
t
Sample Problem 14

## Slide 68
The magnitude and direction of the velocities of two identical frictionless balls before they strike each other are as shown. Assuming e = 0.9, determine the magnitude and direction of the velocity of each ball after the impact.
SOLUTION:
Resolve the ball velocities into components normal and tangential to the contact plane.
Tangential component of momentum for each ball is conserved.
Total normal component of the momentum of the two ball system is conserved.
The normal relative velocities of the balls are related by the coefficient of restitution.
Solve the last two equations simultaneously for the normal velocities of the balls after the impact.
Sample Problem 15

## Slide 69
SOLUTION:
Resolve the ball velocities into components normal and tangential to the contact plane.
Tangential component of momentum for each ball is conserved.
Total normal component of the momentum of the two ball system is conserved.
Sample Problem 15

## Slide 70
The normal relative velocities of the balls are related by the coefficient of restitution.
Solve the last two equations simultaneously for the normal velocities of the balls after the impact.
Sample Problem 15

## Slide 71
Ball B is hanging from an inextensible cord. An identical ball A is released from rest when it is just touching the cord and acquires a velocity v0 before striking ball B. Assuming perfectly elastic impact (e = 1) and no friction, determine the velocity of each ball immediately after impact.
SOLUTION:
Determine orientation of impact line of action.
The momentum component of ball A tangential to the contact plane is conserved.
The total horizontal momentum of the two ball system is conserved.
The relative velocities along the line of action before and after the impact are related by the coefficient of restitution.
Solve the last two expressions for the velocity of ball A along the line of action and the velocity of ball B which is horizontal.
Group Problem Solving

## Slide 72
SOLUTION:
Determine orientation of impact line of action.
The momentum component of ball A tangential to the contact plane is conserved.
The total horizontal (x component) momentum of the two ball system is conserved.
Group Problem Solving

## Slide 73
The relative velocities along the line of action before and after the impact are related by the coefficient of restitution.
Solve the last two expressions for the velocity of ball A along the line of action and the velocity of ball B which is horizontal.
Group Problem Solving

## Slide 74
A 30 kg block is dropped from a height of 2 m onto the 10 kg pan of a spring scale. Assuming the impact to be perfectly plastic, determine the maximum deflection of the pan. The constant of the spring is k = 20 kN/m.
SOLUTION:
Apply the principle of conservation of energy to determine the velocity of the block at the instant of impact.
Since the impact is perfectly plastic, the block and pan move together at the same velocity after impact. Determine that velocity from the requirement that the total momentum of the block and pan is conserved.
Apply the principle of conservation of energy to determine the maximum deflection of the spring.
Sample Problem 17

## Slide 75
SOLUTION:
Apply principle of conservation of energy to determine velocity of the block at instant of impact.
Determine velocity just after impact from requirement that total momentum of the block and pan is conserved.
Sample Problem 17

## Slide 76
Initial spring deflection due to pan weight:
Apply the principle of conservation of energy to determine the maximum deflection of the spring.
Sample Problem 17

## Slide 77
A 2-kg block A is pushed up against a spring compressing it a distance x= 0.1 m. The block is then released from rest and slides down the 20º incline until it strikes a 1-kg sphere B, which is suspended from a 1 m inextensible rope. The spring constant k=800 N/m, the coefficient of friction between A and the ground is 0.2, the distance A slides from the unstretched length of the spring d=1.5 m, and the coefficient of restitution between A and B is 0.8. When a=40o, find (a) the speed of B (b) the tension in the rope.
SOLUTION:
This is a multiple step problem. Formulate your overall approach.
Use work-energy to find the velocity of the block just before impact
Use conservation of momentum to determine the speed of ball B after the impact
Use work energy to find the velocity at a
Use Newton’s 2nd Law to find tension in the rope
Group Problem Solving

## Slide 78
Given: mA= 2-kg mB= 1-kg, k= 800 N/m, mA =0.2, e= 0.8
Find (a) vB (b) Trope
Use work-energy to find the velocity of the block just before impact
Determine the friction force acting on the block A
Sum forces in the y-direction
Solve for N
Group Problem Solving

## Slide 79
Set your datum, use work-energy to determine vA at impact.
Determine values for each term.
Substitute into the Work-Energy equation and solve for vA
Group Problem Solving

## Slide 80
Use conservation of momentum to determine the speed of ball B after the impact
Draw the impulse diagram
Note that the ball is constrained to move only horizontally immediately after the impact.
Apply conservation of momentum in the x direction
Use the relative velocity/coefficient of restitution equation
(1)
(2)
Solve (1) and (2) simultaneously
Group Problem Solving

## Slide 81
Use work energy to find the velocity at a
Set datum, use Work-Energy to determine vB at a= 40o
Determine values for each term.
Substitute into the Work-Energy equation and solve for vA
Group Problem Solving

## Slide 82
Use Newton’s 2nd Law to find tension in the rope
Draw your free-body and kinetic diagrams
Sum forces in the normal direction
Determine normal acceleration
Substitute and solve
Group Problem Solving

## Slide 83
If the coefficient of restitution is smaller than the 0.8 in the problem, the tension T will be…
Smaller
Bigger
If the rope length is smaller than the 1 m in the problem, the tension T will be…
Smaller
Bigger
If the coefficient of friction is smaller than 0.2 given in the problem, the tension T will be…
Smaller
Bigger
If the mass of A is smaller than the 2 kg given in the problem, the tension T will be…
Smaller
Bigger
Compare the following statement to the problem you just solved.
Concept Question

## Slide 84
Forces and Accelerations
Velocities and Displacements
Velocities and Time
Approaches to Kinetics Problems
Newton’s Second Law (last chapter)
Work-Energy
Impulse-Momentum
Summary

## Slide 85
Acknowledgement
NPTEL lectures on Engineering Mechanics
Beer & Johnston, Vector Mechanics for Engineers
Meriam & Kraige, Engineering Mechanics
Problems taken from internet sources
Timoshenko & Young, Engineering Mechanics